SAFETY DATA SHEET

PRODUCT NAME:			ENGAGE ACCELERATE

PRODUCT CODE:			-

1.IDENTIFICATION OF THE SUBSTANCE/PREPARATION AND THE COMPANY

1.1  Product Identifier

TRADE NAME				ENGAGE ACCELERATE

OTHER NAMES

CHEMICAL SYNONYMS		Anionic surfactant

1.2  Relevant identified uses of the substance or mixture and uses advised against

IDENTIFIED USES			Turf Wetting Surfactant

1.3  Details of the supplier of the safety data sheet

SUPPLIER:				GBR TECHNOLOGY LTD

UNIT 42 EASTER PARK

BENYON ROAD

SILCHESTER

READING, BERKS  RG7 2PQ

Tel: 0118 9820567	Fax: 0118 9820590

Email address of person responsible	info@gbrtech.co.uk

1.4  Emergency telephone number

SUPPLIER:				0118 9820567

HOURS OF OPERATION:		Monday to Friday 0830 – 17:00 HRS

INFORAMTION LIMITATIONS:		Not applicable

2. HAZARD INDENTIFICATION

2.1  Classification of the substance or mixture

PRODUCT DEFINITION:		Substance

Classification according to Regulation (EC) No. 1272/2008 [CLP/GHS]

Skin Corr./Irrit. 2

Eye Dam./Irrit. 1

Aquatic Chronic 2

H318, H315, H411

For the classifications not written out in full in this section the full text can be found in section 16.

2.2  Label elements:

PICTOGRAM

SIGNAL WORD:			Danger

HAZARD STATEMENTS:

| H318 | Causes serious eye damage. |
| --- | --- |
| H315 | Causes skin irritation. |
| H411 | Toxic to aquatic life with long lasting effects. |

PRECAUTIONARY STATEMENTS (PREVENTION)

| P280 | Wear protective gloves and eye/face protection. |
| --- | --- |
| P273 | Avoid release to the environment. |
| P264 | Wash with plenty of water and soap thoroughly after handling. |

PRECAUTIONARY STATEMENTS (RESPONSE)

| P305 + P351 + P338 | IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. |
| --- | --- |
| P310 | Immediately call a POISON CENTER or doctor/physician. |
| P303 + P352 | IF ON SKIN (or hair): Wash with plenty of soap and water. |
| P391 | Collect spillage. |
| P362 + P364 | Take off contaminated clothing and wash it before reuse. |

PRECAUTIONARY STATEMENTS (DISPOSAL)

| P501 | Dispose of contents/container to hazardous or special waste collection point. |
| --- | --- |

Labelling of special preparations (GHS):

This surfactant complies with the biodegradability criteria as laid down in Regulation (EC) No.648/2004 on detergents. Data to support this assertion are held at the disposal of the competent authorities of the Member States and will be made available to them at their direct request or at the request of a detergent manufacturer.

3. COMPOSITION/INFORMATION ON INGREDIENTS

SUBSTANCE/MIXTURE:		Substance

Chemical Nature				Anionic surfactant in water/solvent

| Product/ingredient name 2,2-Dimethylpropane-1,3-diol Docusate sodium Bis(2-ethylhexyl) maleate | Identifiers CAS Number: 126-30-7 EC-Number: 204-781-0 REACH registration number: 01-2119480396-30 CAS Number: 577-11-7 EC-Number: 209-406-4 REACH registration number: 01-2119491296-29 CAS Number: 142-16-5 EC-Number: 205-524-5 REACH registration number: 01-2119552449-30 | % >= 5 % - < 15 % >= 50 % - < 75 % >= 3 % - < 10 % | Regulation (EC) No. 1272/2008 [CLP] Eye Dam./Irrit. 1 H318 Skin Corr./Irrit. 2 Eye Dam./Irrit. 1 H318, H315 STOT RE (Kidney) 2 (oral) Aquatic Chronic 1 M-factor acute: 1 M-factor chronic: 1 H373, H410 |
| --- | --- | --- | --- |

There are no additional ingredients present which, within the current knowledge of the supplier and in the concentrations applicable, are classified as hazardous to health or the environment, are PBTs or vPvBs or have been assigned a workplace exposure limit and hence require reporting in this section.

4. FIRST AID MEASURES

4.1  Description of first aid measures

Eye contact:	Immediately flush eyes with plenty of water for 15 minutes, occasionally lifting the upper and lower eyelids.  Check for and remove and contact lenses.  Get medical attention if irritation occurs.

Inhalation:  	Remove victim to fresh air and keep at rest in a position comfortable for breathing.  Seek medical attention and immediately administer a corticosteroid from a metered dose inhaler.

Skin contact:	Flush contaminated skin with plenty of water.  Remove contaminated clothing and shoes.  Apply sterile dressings, consult a skin specialist.

Ingestion:	Wash out mouth with water.  Then drink 200-300ml of water, and seek medical attention.

4.2  Most important symptoms and effects, both acute and delayed

Symptoms: The most important known symptoms and effects are described in the labelling (see section 2) and/or in section 11., Further important symptoms and effects are so far not known.

4.3  Indication of any immediate medical attention and special treatment needed

Notes to physician:	Treat symptomatically

Specific treatments:	No specific treatment.

5. FIRE-FIGHTING MEASURES

5.1  Extinguishing media

Suitable extinguishing media:	Use a suitable extinguishing agent – water spray, dry powder, foam.

Unsuitable extinguishing media:	None Known

5.2  Specific hazards arising from the substance or mixture

Hazards from the substance:	Evolution of fumes/fog.

Hazardous combustion products:	None Known.

5.3  Advice for firefighters

Special precautions for firefighters: Promptly isolate the scene by removing all persons form the vicinity of the incident if there is a fire.  No action shall be taken involving any personal risk or without suitable training.

Special protective equipment for	Fire-fighter should wear appropriate protective equipment and self-

firefighters:	contained breathing apparatus (SCBA) with a full face-piece operated in positive pressure mode.  Clothing for fire-fighters (including helmets, protective boots and gloves) conforming to European standard EN 469 will provide a basic level of protection for chemical incidents.

Additional information:	Non Provided

6. ACCIDENTAL RELEASE MEASURES

6.1  Personal precautions, protective equipment and emergency procedures

Personnel:	High risk of slipping due to leakage/ spillage of product. Do not walk through spilt material.  Put on appropriate personal protective equipment. Use personal protective clothing.  Information regarding personal protective measures see Chapter 8.

.

6.2   Environmental Precautions:	Avoid dispersal of spilt material.  Inform the relevant authorities of the product has caused environmental pollution (sewers, waterways, soil or air)  Contain contaminated water. Do no discharge into drains/surface waters/groundwaters.

6.3   Methods and Materials for containment and cleaning up

Spill:	Stop leak if without risk.  Move containers away from spill area.  Prevent entry into sewers, water courses, basements or confined areas.  Contain and collect spillage with non-combustible, absorbent material e.g: sand, earth, vermiculite or diatomaceous earth and place in container for disposal according to local regulations.  Dispose of via a licensed waste disposal contractor.

6.4.   Reference to other sections:	See Section 1 for emergency contact information.

See section 8 for information on appropriate personal protective equipment

See section 13 for additional waste treatment information.

7. HANDLING AND STORAGE

The information in this section contains generic advice and guidance.  The list of identified uses in section 1 should be consulted for any available use-specific information provided in the Exposure Scenario(s).

7.1 	Precautions for safe handling

Avoid aerosol formation.

Protection against fire and explosion:

Take precautionary measures against static discharges.

7.2	Conditions for safe storage, including any incompatibilities:

Suitable materials for containers: Low density polyethylene (LDPE), Stainless steel 1.4301 (V2), Stainless steel 1.4401, glass, High density polyethylene (HDPE)

Further information on storage conditions: Keep container tightly closed and dry; store in a cool place.

Storage stability:

Storage temperature: <= 70 °C

The product is not damaged by low temperatures or by frost.

Protect from temperatures above: 70 °C

Properties of the product change irreversibly on exceeding the limit temperature.

7.3	Specific end use(s)

For the relevant identified use(s) listed in Section 1 the advice mentioned in this section 7 is to be observed

8. EXPOSURE CONTROLS AND PERSONAL PROTECTION

The information in this section contains generic advice and guidance.  The list of identified uses in section 1 should be consulted for any available use-specific information provided in the Exposure Scenario(s).

8.1	Control Parameters

OCCUPATIONAL EXPOSURE LIMITS: No limits known

8.2	Exposure Controls

Respiratory protection:

Suitable respiratory protection for higher concentrations or long-term effect: Gas filter for gases/vapours of organic compounds (boiling point >65 °C, e. g. EN 14387 Type A)

Hand protection:

Chemical resistant protective gloves (EN 374)

Suitable materials for short-term contact (recommended: At least protective index 2, corresponding > 30 minutes of permeation time according to EN 374)

butyl rubber (butyl) - 0.7 mm coating thickness

nitrile rubber (NBR) - 0.4 mm coating thickness

Supplementary note: The specifications are based on tests, literature data and information of glove manufacturers or are derived from similar substances by analogy. Due to many conditions (e.g. temperature) it must be considered, that the practical usage of a chemical-protective glove in practice may be much shorter than the permeation time determined through testing.

Manufacturer's directions for use should be observed because of great diversity of types.

Eye protection:

Tightly fitting safety goggles (cage goggles) (e.g. EN 166) and face shield.

Body protection:

Body protection must be chosen depending on activity and possible exposure, e.g. apron, protecting boots, chemical-protection suit (according to EN 14605 in case of splashes or EN ISO 13982 in case of dust).

General safety and hygiene measures

Wearing of closed work clothing is required additionally to the stated personal protection equipment. No eating, drinking, smoking or tobacco use at the place of work. Handle in accordance with good industrial hygiene and safety practice.

Environmental exposure controls

For information regarding environmental exposure controls, see Section 6.

9. PHYSICAL AND CHEMICAL PROPERTIES

9.1 Information on basic physical and chemical properties

Appearance

Physical State:			Liquid

Colour: 				Yellowish

Odour:				Product Specific

Odour Threshold:			Not determined

pH:				Approx. 6.5 (50g/lt, 23°C)

Melting / Freezing point:		Approx -15°C

Boiling point 	 		Approx. 85°C

Flash Point:			> 166°C

Evaporation Rate:		Not determined

Flammability:	Not highly flammable

Upper 		18.8% (V) Value is calculated from the component data

flammability or

explosive limits:

Lower		1.37% (V) Value is calculated form the component data

flammability or

explosive limits:

Vapour Pressure:			20mBar (20°C), 97mBar (50°C) (DIN 51794)

Vapour Density:			Not Available

Relative Density:			1.11g/cm3 @ 20°C

Solubility (ies):			Moderately soluble in water

Partition Coefficient:

n-octanol/water:			1.0

Ignition Temperature:		> 200°C

Decomposition Temperature:	> 300°C

Explosive Properties:	Not explosive.

Oxidising Properties:	Not Available

Viscosity:	Approx. 250 mPa.S (23°C)

9.2	Other Information

Miscibility with water:		miscible

10. STABILITY AND REACTIVITY

10.1	Reactivity:		No hazardous reactions if stored and handled as prescribed/ indicated.

No corrosive effects to metal

10.2	Chemical Stability:	The product is stable if stored and handled as prescribed/indicated

10.3	Possibility of hazardous

reactions:	No hazardous reactions when stored and handled as prescribed/ indicated.

10.4	Conditions to Avoid:	See Section 7 – Handling and Storage

10.5	Incompatible Materials:	Avoid contact with: caustics, halogens, alkalies, acids.

10.6	Hazardous decomposition

products:	No hazardous decomposition products when stored and handled as prescribed/ indicated.

11. TOXICOLOGICAL INFORMATION

11.1. Information on toxicological effects

Acute toxicity

Experimental/calculated data:

LD50 rat (oral): > 2,000 - 5,000 mg/kg (calculated)

ATE (by inhalation): > 20 mg/l (calculated)

Determined for vapour

ATE (by inhalation): > 5 mg/l (calculated)

ATE (dermal): > 5,000 mg/kg (calculated)

Information on: Docusate sodium

Assessment of acute toxicity:

Of low toxicity after single ingestion. Virtually nontoxic after a single skin contact. Virtually nontoxic by inhalation.

----------------------------------

Irritation

Experimental/calculated data:

Skin corrosion/irritation rabbit: Irritant. (other)

Serious eye damage/irritation rabbit: irreversible damage (other)

Information on: Docusate sodium

Assessment of irritating effects:

Skin contact causes irritation. May cause severe damage to the eyes.

Information on: 2,2-Dimethylpropane-1,3-diol

Assessment of irritating effects:

Not irritating to the skin. May cause severe damage to the eyes.

Information on: Bis(2-ethylhexyl) maleate

Assessment of irritating effects:

Not irritating to the eyes. Skin contact causes slight irritation.

----------------------------------

----------------------------------

Respiratory/Skin sensitization

Assessment of sensitization:

No data available.

Germ cell mutagenicity

Assessment of mutagenicity:

No data available.

Carcinogenicity

Assessment of carcinogenicity:

No data available.

Reproductive toxicity

Assessment of reproduction toxicity:

No data available.

Developmental toxicity

Assessment of teratogenicity:

Based on available Data, the classification criteria are not met.

Information on: Docusate sodium

Assessment of teratogenicity:

The substance did not cause malformations in animal studies; however, toxicity to development was observed at high doses which impaired body weight gain in parental animals.

----------------------------------

Specific target organ toxicity (single exposure)

Remarks: No data available.

Repeated dose toxicity and Specific target organ toxicity (repeated exposure)

Assessment of repeated dose toxicity:

Based on available Data, the classification criteria are not met.

Information on: Bis(2-ethylhexyl) maleate

Assessment of repeated dose toxicity:

The substance may cause damage to the kidney even after repeated ingestion of low doses, as shown in animal studies. The product has not been tested. The statement has been derived from substances/products of a similar structure or composition.

----------------------------------

Aspiration hazard

No aspiration hazard expected.

Other relevant toxicity information

The product has not been tested. The statements on toxicology have been derived from the properties of the individual components.

12. ECOLOGICAL INFORMATION

12.1	Toxicity

Toxicity to fish:

LC50 (96 h) > 10 - 100 mg/l, Leuciscus idus (OECD 203; ISO 7346; 84/449/EEC, C.1)

Aquatic invertebrates:

EC50 (48 h) > 1 - 10 mg/l, Daphnia magna (Directive 79/831/EEC)

Aquatic plants:

EC50 (72 h) > 10 - 100 mg/l a.i. (growth rate), Desmodesmus subspicatus (Guideline 92/69/EEC, C.3, static)

Nominal concentration.

No observed effect concentration (72 h) > 0.01 - 0.1 mg/l (growth rate), Pseudokirchneriella subcapitata (OECD Guideline 201, static)

The statement of the toxic effect relates to the analytically determined concentration.

Microorganisms/Effect on activated sludge:

EC50 (96 h) > 10,000 mg/l (DIN 38412 Part 27 (draft))

Chronic toxicity to fish:

No data available.

Chronic toxicity to aquatic invertebrates:

No data available.

Assessment of terrestrial toxicity:

No data available concerning terrestrial toxicity.

12.2	Persistence and degradability

Elimination Information:

> 90 % Methylene blue-active substance (mod. OECD 303A)

> 60 % CO2 formation relative to the theoretical value (28 d) (OECD 301B; ISO 9439; 92/69/EEC, C.4-C) (activated sludge, domestic) Readily biodegradable.

12.3	Bioaccumulative Potential:	Accumulation in organisms is not to be expected.

12.4	Mobility in Soil

Adsorption			to solid phase is possible

Mobility:	The substance will not evaporate into the atmosphere from the water surface.  Adsorption to solid soil phase is possible.

12.5	Results of PBT and vPvB assessment

According to Annex XIII of Regulation (EC) No.1907/2006 concerning the Registration, Evaluation, Authorisation and Restriction of Chemicals (REACH): The product does not fulfil the criteria for PBT (Persistent/bioaccumulative/toxic) and vPvB (very persistent/very bioaccumulative).

12.6	Other adverse effects:		No known significant effects or critical hazards

12.7	Additional information:

Sum parameter

Chemical oxygen demand (COD): 1,660 mg/g

Biochemical oxygen demand (BOD) Incubation period 5 d: 135 mg/g

Adsorbable organically-bound halogen (AOX):

This product contains no organically-bound halogen.

Add. remarks environm. fate & pathway:

Treatment in biological waste water treatment plants has to be performed according to local and administrative regulations.

Other ecotoxicological advice:

Inhibition of degradation activity in activated sludge is not to be anticipated during correct introduction of low concentrations. The product has not been tested. The statements on ecotoxicology have been derived from the properties of the individual components. Do not allow to enter soil, waterways or waste water channels.

13. DISPOSAL CONSIDERATIONS

13.1	Waste Treatment Methods

Must be disposed of or incinerated in accordance with local regulations.

The UK Environmental Protection (Duty of Care) Regulations (EP) and amendments should be noted (United Kingdom).

This product and any uncleaned containers must be disposed of as hazardous waste in accordance with the 2005 Hazardous Waste Regulations and amendments (United Kingdom)

Contaminated packaging:

Uncontaminated packaging can be re-used.

Packs that cannot be cleaned should be disposed of in the same manner as the contents.

14. TRANSPORT INFORMATION

|  | ADR / RID | ADN / ADNR | IMDG | IATA |
| --- | --- | --- | --- | --- |
| 14.1 UN Number | UN 3082 | UN 3082 | UN 3082 | UN 3082 |
| 14.2 Proper Shipping Name | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, LIQUID, N.O.S (contains BIS(2-ETHYLHEXYL) MALEATE) |
| 14.3 Transport Hazard Class(es) | 9 | 9 | 9 | 9 |
| 14.4 Packing Group | III | III | III | III |
| 14.5 Environmental Hazards | Environmentally Hazardous | Environmentally Hazardous | Marine Pollutant | Environmentally Hazardous |
| 14.6 Special Precautions for user | Not Available | Not Available | Not Available | Not Available |
| Additional Information | - | - | - | - |

14.7	Transport in Bulk according

To Annex II of

MARPOL 73/78 and

The IBC Code:			Not Available

15. REGULATORY INFORMATION

15.1	Prohibitions, Restrictions and Authorizations

Annex XVII of Regulation (EC) No 1907/2006: Number on List: 3

If other regulatory information applies that is not already provided elsewhere in this safety data sheet, then it is described in this subsection.

The data should be considered when making any assessment under the Control of Substances Hazardous to Health Regulations (COSHH), and related guidance, for example, 'COSHH Essentials' (United Kingdom).

This product may be subject to the Control of Major Accident Hazards Regulations (COMAH), and amendments if specific threshold tonnages are exceeded (United Kingdom).

15.2. Chemical Safety Assessment

Advice on product handling can be found in sections 7 and 8 of this safety data sheet.

16.  OTHER INFORMATION

Information on intended use: This product is of industrial quality and unless otherwise specified or agreed intended exclusively for industrial use. This includes the mentioned and recommended usage. Any other intended applications should be discussed with the manufacturer. In particular this concerns the application for products that are the object of special standards and regulations.

| Full text of the classifications, including the hazard classes and the hazard statements, if mentioned in section 2 or 3: Skin Corr./Irrit. | Skin corrosion/irritation |
| --- | --- |
| Eye Dam./Irrit. | Serious eye damage/eye irritation |
| Aquatic Chronic | Hazardous to the aquatic environment - chronic |
| STOT RE | Specific target organ toxicity — repeated exposure |
| H318 | Causes serious eye damage. |
| H315 | Causes skin irritation. |
| H411 | Toxic to aquatic life with long lasting effects. |
| H373 | May cause damage to organs (Kidney) through prolonged or repeated exposure (oral). |
| H410 | Very toxic to aquatic life with long lasting effects. |

Date of Printing:				31 May 2023

Date of Issue / Date of revision:		31 May 2023

Date of Previous Issue Version:		-

Version:					1

Prepared by:				ADF

For Copy of SDS:			Email: info@gbrtech.co.uk

0118   9820 567

For product Safety Information:		Email: info@gbrtech.co.uk

0118   9820 567

--------------------------------------------------------------------------------------------------------------------------------

To the best of our knowledge , the information contained herein is accurate.  However, neither the above-named supplied, nor any of its subsidiaries, assumes any liability whatsoever for the accuracy or completeness of the information contained herein.

Final determination of suitability of any material is the sole responsibility of the user.  All materials may present unknown hazards and should be used with caution.  Although certain hazards are described herein, we cannot guarantee that these are only hazards that exist.